## Slide 1: CHBE 424: Chemical Reaction Engineering
Introduction & Lecture 1

## Slide 2: What is Chemical Reaction Engineering (CRE) ?
Understanding how chemical reactors work lies at the heart of almost every chemical processing operation.
Design of the reactor is no routine matter, and many alternatives can be proposed for a process. Reactor design uses information, knowledge and experience from a variety of areas - thermodynamics, chemical kinetics, fluid mechanics, heat and mass transfer, and economics.
CRE is the synthesis of all these factors with the aim of properly designing and understanding the chemical reactor.
Chemical process
Raw
material
Separation Process
Products
By-products
Separation Process

## Slide 3: How do we design a chemical reactor?
Type & size
Maximize the space-time yield of the desired product (productivity lb/hr/ft3)
Stoichiometry
Kinetics
Basic molar balances
Fluid dynamics
Reactor volume
Use a lab-scale reactor to determine the kinetics!

## Slide 4: Reactor Design
Reaction
Stoichiometry
Kinetics: elementary vs non-elementary
Single vs multiple reactions
Reactor
Isothermal vs non-isothermal
Ideal vs nonideal
Steady-state vs nonsteady-state

## Slide 5: What type of reactor(s) to use?
in
out
Continuously Stirred
Tank Reactor (CSTR)
Well-mixed batch reactor
Plug flow reactor (PFR)

## Slide 6: What size reactor(s) to use?
Answers to this questions are based on the desired conversion, selectivity and kinetics
Reactor type &
size
Conversion
&
selectivity
Kinetics
Material &
energy
balances

## Slide 7: Chemical Reaction
A detectable number of molecules have lost their identity and assumed a new form by a change in the kind or number of atoms in the compound and/or by a change in the atoms’ configuration
  Decomposition
  Combination
  Isomerization
Rate of reaction
  How fast a number of moles of one chemical species are being consumed to form another chemical species

## Slide 8: Rate Law for rj
rA: the rate of formation of species A per unit volume [e.g., mol/m3•s]
-rA: the rate of a consumption of species A per unit volume
rj depends on concentration and temperature:
1st order in A, 1st order in B, 2nd order overall
nth order in A
Michaelis-Menton: common in enzymatic reactions

## Slide 9
Basic Molar Balance (BMB)
Rate of flow of j into system
-
Rate of flow of j out of system
+
Rate of generation of j by chemical rxn
-
Rate of decomposition of j
=
Rate of
accumulation
combine
Nj: moles j in system at time t
System volume
Fj0
Fj
Gj
in
-
out
+
generation
=
accumulation

## Slide 10
Basic Molar Balance (BMB)
Rate of flow of j into system
-
Rate of flow of j out of system
+
Rate of generation of j by chemical rxn
-
Rate of decomposition of j
=
Rate of
accumulation
If the system is uniform throughout its entire volume, then:
Moles j generated per unit time
(mol/s)
=
Moles generated per unit time and volume (mol/s•m3)
Volume
(m3)

## Slide 11: Non-Uniform Generation
DV
If rj varies with position (because the temperature or concentration varies) then rj1 at location 1 is surrounded by a small subvolume DV within which the rate is uniform
Rate is rj1 within this volume
DV
Rate is rj2 within this volume
lim
m→∞
DV→0
1
1
1
y
x
z
Plug in rj and integrate over x, y, and z
system

## Slide 12: Basic Molar Balance Equations
In
Out
-
+
Generation
=
Accumulation
Next time: Apply BME to ideal batch, CSTR, & PFR reactors
System volume
Fj0
Fj
Gj

## Slide 13: Review of Frequently Encountered Math Concepts

## Slide 14: Basic Math Review
Solve for X:
Example: Problems that Contain Natural Logs

## Slide 15: Review of Basic Integration
For n≠1:
For n=1:
Solve for t:

## Slide 16
Do NOT move t or c outside of the integral
From Appendix A:
0
Solve for c:
ε is a constant