## Slide 1: Review: Derive –rA = f(XA)
Relate all V(u) to XA
Put together
Relate all rj to Cj
nj ≡ stoichiometric coefficient
Relate all Cj(XA) to V(u)
 for products, ⊖ for reactants
Batch:
Flow:
Batch:
Flow:
Batch
& Flow:
Now that Cj is in terms of XA, we can write the rate law in terms of XA

## Slide 2: Review: Stoichiometric Tables
Species | Feed rate (mol/time) | Change in reactor (mol/time) | Effluent rate from reactor (mol/time)
A | FA0 | -FA0XA | FA = FA0 (1–XA)
B | FB0 = QBFA0 | nBFA0XA | FB = FA0 (QB+ nBXA)
C | FC0 = QCFA0 | nCFA0XA | FC = FA0 (QC+ nCXA)
D | FD0 = QDFA0 | nDFA0XA | FD = FA0 (QD+ nDXA)
I | FI0 = QIFA0 | --- | FI =FI0
Total | FT0 | dFA0XA | FT = FT0 + dFA0XA
FA0
FB0
FC0
FD0
FI0
FA
FB
FC
FD
FI
nj ≡ stoichiometric coefficient
 for products, ⊖ for reactants
In
Out

## Slide 3: L5: Reactor Design Recipe and Reactor Scale-Up (Sizing)
Goal: Develop an algorithm that combines reactor design equations with reaction rates for the design of different reactors

## Slide 4: The Logic of Isothermal Reactor Design
In
Out
-
+
Generation
=
Accumulation
1. Set up mole balance for specific reactor
2. Derive design eq. in terms of XA for each reactor
Batch
CSTR
PFR
3. Put Cj is in terms of XA and plug into rA
4. Plug rA into design eq and solve for the time (batch) or volume (flow) required for a specific XA
Today and next week!
(We will always look conditions where Z0=Z)

## Slide 5: Batch Reactor Operation (1)
Batch Volume is constant, V=V0
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
A → B -rA = kCA2
2nd order reaction rate
Calculate the time required for a conversion of XA in a constant V batch reactor

## Slide 6: Batch Reactor Operation (2)
Calculate the time required for a conversion of XA in a constant V batch reactor
Evaluate
Rearrange to get like variables together
k is constant for an isothermal reaction
Time required to achieve XA for 2nd order rxn
Integrate
A → B -rA = kCA2
2nd order reaction rate

## Slide 7: Batch Reactor Operation (3)
Batch Volume is constant, V=V0
Calculate the time required for a conversion of XA in a constant V batch reactor
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
A → B -rA = kCA
1st order reaction rate
Mole balance as a function of conversion

## Slide 8: Batch Reactor Operation (4)
Calculate the time required for a conversion of XA in a constant V batch reactor
Evaluate to solve for time
Rearrange to get like variables together
k is constant for an isothermal reaction
Time required to achieve XA for 1st order rxn
Integrate
Mole balance as in terms of XA:
A → B -rA = kCA
1st order reaction rate
Remember:
Confused about the integration? See the next slide

## Slide 9: Batch Reactor Operation (4)
Calculate the time required for a conversion of XA in a constant V batch reactor
Integrate
A → B -rA = kCA
1st order reaction rate
0=ln(1)
Remember:

## Slide 10: Typical Cycle Time for a Batch Polymerization
Activity | Time (h)
1. Charge feed to the reactor and agitate (tf) | 1.5 - 3.0
2. Heat to reaction temperature (te) | 0.2 – 2.0
3. Carry out reaction (tR) | (varies)
4. Empty and clean reactor (tc) | 0.5 – 1.0
Total time excluding reaction | 3.0 – 6.0
Total Cycle Time tt = tf + te + tR + tc
Total Cycle Time tt for a batch process is much longer than the reaction time because it takes time to set up, heat, and clean the reactor each time it is used

## Slide 11: CSTR Operation (1)
Calculate the CSTR volume required to get a conversion of XA
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
A → B -rA = kCA
Liquid-phase 1st order reaction rate
Put FA0 in terms of CA0
Volume required to achieve XA for 1st order rxn (u0=u)

## Slide 12: Scaling CSTRs
Space time t (residence time) required to achieve XA for 1st order irreversible rxn
Chemical engineers are involved in scaling up a laboratory scale reaction to the pilot plant scale or full-scale reactor
If one knows the volume of the pilot-scale reactor required to achieve XA, how is this information used to achieve XA in a larger reactor?
k in the small reactor is the same as k in the bigger reactor
Want XA in the small reactor to be the same as XA in the bigger reactor
u0 in the small reactor must be different from u0 in the bigger reactor
Suppose for a 1st order irreversible liquid-phase reaction:
Separate variables we will
vary from those held constant
So the reactor volume V must be proportional to the volumetric flow rate u0
How?

## Slide 13: Scaling CSTRs with Spacetime t
A → B -rA = kCA
So if you know the spacetime t required to get a conversion of XA in a CSTR, you can use that to achieve the same XA in a different size CSTR
1st order reaction rate
What t is required to achieve a specific XA?
CSTR relationship between t and XA for 1st order liquid-phase rxn (isothermal and V = V0)
Space time t (residence time) required to achieve XA for 1st order irreversible rxn
Rearrange to get XA in terms of t:

## Slide 14: Damköhler Number, Da
Estimates the degree of conversion that can be obtained in a flow reactor
First order irreversible reaction:
1st order irreversible reaction
Second order irreversible reaction:
2nd order irreversible reaction
How is XA related to Da in a first order irreversible reaction in a flow reactor?
Substitute
From previous slide:

## Slide 15: Damköhler Number, Da
If Da<0.1 for this 1st order irreversible rxn in a flow reactor, then
Estimates the degree of conversion that can be obtained in a flow reactor
Relate XA to Da for a 1st order irreversible rxn in a flow reactor:
If Da>10 for this 1st order irreversible rxn in a flow reactor, then
1st order irreversible rxn

## Slide 16: Sizing CSTRs for 2nd Order Rxns
Mole balance
Rate laws
Stoichiometry
Combine
or
Calculate the CSTR volume required to get a conversion of XA
A → B -rA = kCA2
Liquid-phase 2nd order reaction rate
In terms of conversion?
In terms of space time?
In terms of XA as a function of Da?
2nd order liquid irreversible reaction

## Slide 17: CSTRs in Series
CA0u0
CA1u
CA2u
u0 = u
Effluent of reactor 1 is input for reactor 2, no change in u
A first order reaction is carried out isothermally using 2 CSTRs that are the same size, and u and k are the same in both reactors (t1 = t2 = t & k1 = k2 = k)
Relate CA2 to CA1, k, & t
Mole balance CSTR2
Rate law CSTR2
Stoichiometry CSTR2
Combine for CSTR2
Determine V1 for 1st CSTR using our standard procedure. For 2nd CSTR:
Skip this step for now.

## Slide 18: CSTRs in Series, CA1
CA0u0
CA1u
CA2u
A first order reaction is carried out isothermally using 2 CSTRs that are the same size, and u and k are the same in both reactors (t1 = t2 = t & k1 = k2 = k)
What is CA1 in terms of t and k?
We know for a single CSTR:
Put XA for 1st CSTR in terms of CA1:
Substitute:
Solve for CA1:
u0 = u
Effluent of reactor 1 is input for reactor 2, no change in u

## Slide 19: CSTRs in Series, CA2
CA0u0
CA1u
CA2u
u0 = u
Effluent of reactor 1 is input for reactor 2
A first order reaction is carried out isothermally using 2 CSTRs that are the same size, and u and k are the same in both reactors (t1 = t2 = t & k1 = k2 = k)
Relate CA2 to k & t
Substitute
1st order irreversible rxn with V1 = V2, t1 = t2 and k1 = k2

## Slide 20: n CSTRs in Series
CA0u0
CA1u
CA2u
u0 = u
For n identical CSTRs, then:
How is conversion related to the # of CSTRs in series?
Put CAn in terms of XAn (XA at the last CSTR):
1st order irreversible liquid phase rxn run in n CSTRs with identical V, t and k
1st order irreversible liquid-phase rxn run in n CSTRs with identical V, t and k
Rate of disappearance of A in the nth reactor:

## Slide 21: Isothermal CSTRs in Parallel
FA0
FA01
FA02
same T, V, u
Subscript i denotes reactor i
FA01 = FA02 = … FA0n
Volume of each CSTR
Molar flow rate of each CSTR
Mole Balance
Conversion achieved by any one of the reactors in parallel is the same as if all the reactant were fed into one big reactor of volume V